MKFLOPPIES README.DOC





          This document gives details of the modus  operandi  used  by
          the  mkfloppies shell script and four other scripts ( mkker-
          nel, mkboot, mknewfs and mkarchive ) that it invokes.

          1.  OBJECTIVE.

               The purpose of these scripts is  to  create  a  set  of
          floppies  which will allow a user to re-create a RISCiX sys-
          tem after either a fatal hard disc  problem,  or  after  re-
          partitioning  and  re-formatting  a hard disc to re-allocate
          storage space. The scripts will rebuild the  system  to  the
          point  where  it  is  possible to go multi-user and to mount
          remote filesystems.  At this point a remote machine  may  be
          mounted  and  files  copied across, files may be transferred
          using tar, or a full restore may be carried out from  backup
          media.

          2.  MEDIA

               It is possible that you may have received these scripts
          on  a  floppy disc.  If that is the case the disc will be in
          (tar,compress,dsplit) format and will  contain  the  scripts
          described  below  for use within RISCiX. The scripts need to
          be copied to the RISCiX directory  /tmp  on  the  hard  disc
          using the following commands :

          # cd /tmp
          # dsplit | uncompress | tar xvf -


          3.  CREATING THE FLOPPIES.

               The four discs will be created by running  the  mkflop-
          pies script.  Alternatively, the discs may be made individu-
          ally by running the appropriate scripts as  detailed  below.
          Note  that  to  run  all  the  scripts it is necessary to be
          logged in as root, and in the /tmp directory.

          3.1.  mkfloppies

               The script `mkfloppies` will create the  four  floppies
          required to rebuild a RISCiX system. It does this by calling
          the following four scripts.



                                October 28, 1992





                                     - 2 -


          3.2.  mkkernel

               This  script  creates  a  floppy  containing  a  RISCiX
          filesystem  configured for optimal file space. A copy of the
          kernel ( /vmunix ) is then installed: Note, if  you  have  a
          1.2  RISCiX  kernel less than version 1.21a then this is the
          kernel supplied with `mkfloppies`, not the original  kernel.
          In  addition  some  files are copied on for use later in the
          re-installation process.

          3.3.  mknewfs

               This script also creates a floppy with a  space  optim-
          ised  RISCiX  filesystem.  The floppy is used to prepare the
          hard disk for the re-installation process.

          It contains the following files:

          /dev/console, fdf1024,  rfdf1024,  kmem,  null,  cmos,  tty,
          rsd0a, rsd0b, rsd0c, rsd0h, sd0a, sd0b, sd0c.

          /sbin/sh, init, halt, scsidm, ls, fsck.

          /usr/sbin/mkfs, newfs, fsirand, cat

          /usr/lib/c:9010241403.11

          /.profile

          Plus a mini termcap...

          /etc/termcap


          3.4.  mkboot

               This script also creates a floppy with a  space  optim-
          ised  RISCiX  filesystem.   It  then installs or creates the
          files and devices required to bring the  R260  up  from  the
          floppy  device and to go multi user when a full three floppy
          restore is done.

          The device nodes comprise :

          /dev/console, fdf1024,  rfdf1024,  kmem,  null,  cmos,  tty,
          rsd0a, rsd0b, rsd0c, rsd0h, sd0a, sd0b, sd0c.

               In addition  to  these,  various  files  and  utilities
          required  to  create  the  new  RISCiX  filesystem  are also
          installed.

          These are :



                                October 28, 1992





                                     - 3 -


          /sbin/sh, init, mount, umount, halt, mknod, chmod, tar.

          /etc/fstab, mtab, utmp, disktab,

          /usr/lib/c:9010241403.11

          /usr/bin/cat

           Plus a mini termcap...

          /etc/termcap

               A script called `mksystem` is  now  created  (  by  the
          `mkboot`  script  itself  )  which  will be used to actually
          create and set up the new RISCiX filesystem.  This script is
          discussed in more detail under the USAGE section.

          3.5.  mkarchive

               The `kernel` along  with  the  `mknewfs`  and  `mkboot`
          discs  contain  enough  utilities  to  create  a  new RISCiX
          filesystem and make it bootable in single-user mode.

               The purpose of the `mkarchive` disc is to create a disc
          containing  enough  utilities to enable the new system to go
          multi user and to mount the network. It also transports some
          other generally useful utilities.

          It contains the following files :

          /usr/sbin/getty

          /etc/gettytab, rc, rc.net, rc.config, ttys, services.

          /sbin/mkdir, hostname, test, fsck, stty, ifconfig,  restore,
          ps, cp, rm, mv.

          /usr/bin/login, kill, rmdir, sh, df, pwd, vi, hostid, csh.

          /usr/share/lib/termcap

          /usr/ucb/more, rlogin, rcp, rusers, ftp.

          /usr/sbin/ping

          /dev/MAKEDEV

               This list may be extended or customised by editing  the
          `mkarchive` shell script.






                                October 28, 1992





                                     - 4 -


          4.  RISCOS files.

               In conjunction with preparing the four floppies as out-
          lined  above  it is vital that backup copies are made of the
          !RISCiX    application    directory,    the    modules    in
          $.App1.!System.Modules,  the $.!Boot file in the RISCOS par-
          tition, the SETCMOS file ( or a note made of its contents ),
          plus any other files that you treasure. It will be necessary
          to reinstall these after reformatting and  partitioning  the
          drive.

          5.  USAGE

               Having used `mkfloppies` to create the four floppy  set
          it  becomes  possible  to  to use them in many scenarios. We
          will consider a few of them here.

          5.1.  RISCiX fails to boot from the hard disc.

               We will examine the possible situation  where  an  R260
          fails to boot after succesfully initiating the boot sequence
          from the RISCOS desktop. The first stage in the RISCiX  boot
          sequence  is the RISCiXFS module and this should be replaced
          first. If this fails to correct the problem the next  possi-
          ble  cause  may well be the kernel ( /vmunix ) itself. Armed
          with our previously prepared `kernel` disc it is now  possi-
          ble to attempt to boot the kernel from the floppy device and
          the rest of RISCiX from the hard disc.

          To do this follow these steps :

          [1] At the RISCOS desktop press the F12 key.

          [2] At the RISCOS command line prompt ( * ), type :

          *co. device fd0 ( Note that the 0 character here is a zero )

          [3] Insert the 'kernel' disc in the floppy drive.

          [4] Press Ctrl and Reset together to reread CMOS ram.

          [5] Click the middle mouse button on the Task Manager icon -
          in  the  shape  of  an  Archimedes 'A', on the desktop. This
          reveals the Task Menu.

          [6] Click the left mouse button on the 'Exit' option  within
          the Task menu.

          [7] Now type the following command :

          *boot vmunix sd0(0,0) sd0(0,1)




                                October 28, 1992





                                     - 5 -


          Note the spaces in the command and the fact that the 0 is  a
          zero.

               If all goes well this  should  eventually  boot  vmunix
          from  the  floppy and take the machine single user:  If this
          succeeds it may well be that vmunix on the hard disc is cor-
          rupt. The floppy may now be mounted and vmunix replaced.

               If this process fails it may be that either init or one
          of the devices is corrupt.

               It should now be noted that it is possible to boot from
          just  two  floppy  discs,  the  `kernel disc`, and one other
          containing a minimal file system.  On this minimal file sys-
          tem  there  is  just  enough  room to squeeze in a few extra
          files. This hopefully explains the existance of the next two
          discs  `mkboot`  and `mknewfs`, in that a file system can be
          created with a very limited toolbox. Hence, by booting  with
          the  kernel  disc  and  using  the  mkboot  disc as the root
          filesystem it will be possible to  mount  the  suspect  file
          system  onto  this  minimal filesystem. An investigation, or
          possible fix may then be made.

               To do this follow points 1 to 6 above  but  in  step  7
          substitute the following command line...

          boot vmunix fd0(0,0) sd0(0,1)

               This will load the kernel from the  floppy  drive,  use
          the floppy drive as the root filesystem and use the internal
          SCSI drive's swap partition for the swap area.

               After the kernel has successfully been loaded from  the
          floppy disc it will wait one minute for the tools disc to be
          inserted.  Eventually the remainder of RISCiX will be loaded
          from  the  second floppy. At this stage it would be possible
          to mount the hard disc, examine the file system,  and  carry
          out repair work.

          N.B. Do not remove the floppy  disc  from  the  drive  after
          booting in this fashion.

          5.2.  Rebuilding RISCiX.

               It may be  that  the  hard  disc  requires  formatting,
          either  to correct a flaw or to re-allocate partition sizes.
          Armed with the four discs prepared  as  outlined  above  the
          procedure for rebuilding RISCiX is as follows:

          [1] At the RISCOS desktop press the F12 key.

          [2] At the RISCOS command line prompt ( * ), type :



                                October 28, 1992





                                     - 6 -


          *co. device fd0 ( Note that the 0 here is a zero )

          [3] Insert the 'kernel' disc in the floppy drive.

          [4] Press Ctrl and Reset together to reread CMOS ram.

          [5] Click the middle mouse button on the Task Manager icon -
          in  the  shape  of  an  Archimedes 'A', on the desktop. This
          reveals the Task Menu.

          [6] Click the left mouse button on the 'Exit' option  within
          the Task menu.

          [7] Now type the following command :

          boot vmunix fd0(0,0) sd0(0,1)

          This will boot RISCiX as explained above.

          [8] Insert the 'mknewfs' disc when prompted.

          [9] Follow the prompts, and run `mknewfs`.

               First this script runs `scsidm`.

               At the scsidm prompt "scsidm>" enter:

          `device /dev/rsd0h`

               Then, at the prompt, type:

          `section`

               This will prompt you for  the  size  of  your  required
          SCSIFS  section ( 16632 blocks - sectors - are standard on a
          new R260's CP3100 drive ).  Answer 'y' to creating UNIX par-
          titions.

               Next at the "scsidm>" prompt type:

          `partition`

               This will create the various RISCiX partitions. You are
          prompted  for the partition numbers ( 0,1 are standard).  In
          a standard configuration partition 0 is the root, and  1  is
          the swap.  You are then prompted for the start and length of
          partition 0, accept the default start blocks, then the start
          of partition 1, followed by its length.

               After this, exit from scsidm with `quit`.

               "mknewfs" will now display the file `/etc/disktab`.



                                October 28, 1992





                                     - 7 -


          Example:

          cp3100:\
                  :ty=winchester:ns#33:nt#8:nc#776:se#512:rm#1:\
                  :pa#171864:ba#4096:fa#1024:\
                  :pb#16364:bb#4096:fb#1024:\
                  :pg#16632:bg#4096:fg#1024:\
                  :ph#204864:bh#4096:fh#1024

               Partition 0 (a) will now be  `newfs`ed,  and  an  empty
          unix filesystem installed.

          [11] Type 'halt' and Return.


          5.3.  Creating a bootable drive.

               After successfully   creating  a  file  system  on  the
          choosen  drive,  if  the same drive is going to be your boot
          device, it is necessary  at  this  point  to  reinstall  the
          RISCOS files.

          [1] Reinstall the required RISCOS files

          [2] Run `setcmos`, from the Desktop.

          [3] Press F12

          [4] *mount 4

          [5] *opt 4,2

          [6] *co. device fd0

          [7] Place kernel floppy in drive.

          [8] Ctrl-Reset.

          [9] Click on the Task Manager "A" icon with the middle  but-
          ton.

          [10] Click on "exit".

          [11] *boot vmunix fd0(0,0) sd0(0,1)

          [12] When prompted change disc to `mkboot`.

          [13] When the machine returns the  "  #  "  prompt  run  the
          `mksystem` script.

          [14] Follow the prompts, and all  necessary  files  will  be
          copied to the hard disc.



                                October 28, 1992





                                     - 8 -


          [15] When file tranfer is complete, halt the machine.

          [16] Insert the kernel floppy.

          [17] Exit from the desktop by clicking on the Task Manager's
          "A" icon with the middle mouse button.

          [18] Click on "Exit".

          [19] *boot vmunix sd0(0,0) sd0(0,1)

          [20] Follow the  prompts  and  run  `cpsys`,  following  the
          prompts once again.

          [21] Halt the machine.

          [22] From the Desktop, press F12.

          [23] *co. device sd0

          [24] Ctrl-Reset.

          [25] Click on the RISCiX icon.

          [26] Select `single user` from from the maintainance menu.

               You are now in a position to edit  configuration  files
          etcetera,  and  mount other storage devices (network, strea-
          mer, discs) to replace the remainder of the filesystem. Note
          it  will be necessary to create the device drivers for these
          additional devices.
























                                October 28, 1992